Safety Test for Second year welding students only

You must earn a 100%(-0) or rewrite each incorrect answer into a true statement 10 times each

Are these statements TRUE or FALSE? (Do not write on this test)

GENERAL SHOP SAFETY TEST

      - Safety training is just as important as training to use the equipment.

      - Electrical extension cords may be used, even if a wire is exposed on them.

      - Wearing proper clothes, eye protection, and the proper use of tools are three important safety items that must be followed.

      - Jewelry should not be worn when working in the shop at any time.

      - Long hair is dangerous around machines and should always be covered or away.

      - You may throw objects across the shop.

      - Report all injuries to the instructor no matter how minor you think it is.

      - Bend over at the waist when picking up shop tools.

      - Check to see if the metal is hot by picking it up.

      - Clean up scraps and spills only during clean up time.

      - There are 2 fire extinguishers, and 2 fire alarms in the Ag shop.

      - All doors in the Ag shop may be used as an exit when any fire alarm sounds.

      - Meet outside on the lawn by the closest baseball field fence organized in a small group in the case of a fire drill.

      - If your clothes catch on fire stop, drop, and roll.

HAND AND POWER TOOL SAFETY

      - Sharp edged tools should be carried in your pocket close to your body.

      - When using power tools, be sure all shields are in place and functioning.

      - Make sure all tools are clean when you put them away in the appropriate spot.

      - Eye protection is not needed if you have the right tool for the job.

      - Loose clothing must be worn around shop equipment.

      - Power switches should be turned off and the tool stopped before setting the tool down.

      - Eye protection is not needed if the tool has the proper shield.

      - All adjustments to the power tools should be made while power is disconnected.

      - A smoking tool should be put away immediately in the tool room.

      - Use your fingers to brush chips away from any components of the drill press.

      - Stock should be securely fastened to prevent twisting during the drilling process.

Check your answer key and make sure your last answer was #25

ABRASIVE CUT OFF SAW SAFETY

      - Face shield should be worn when operating the cut off saw at all times.

      - Stock of length should be supported during cutting.

      - The power should be disconnected while changing the abrasive wheel or making adjustments.

      - The work clamp should be adjusted to properly position the stock and hold it securely against the fence.

      - The operator should remain in the safe work zone until the machine is turned off.

      - There is no serious problem if the wheel wobbles when you turn on the machine.

      - Fresh cuts made by the saw are not dangerous and can be handled.

PEDESTAL GRINDER SAFETY

      - Always check the wheel for cracks or chips before using; damaged wheels should never be used.

      - Wear a face shield and safety glasses, even though the grinder may have a shield.

      - Adjust the tool rest so that it is 1/8 inch from the face of the wheel.

      - The grinding wheel should be used until it is worn down to 1/6 of its original diameter.

      - Using the side of the grinding wheel may cause stress on the grinding wheel and cause it to break.

      - The grinder should reach full speed before it is used.

      - Hold the object you are grinding so that your fingers are in no way close to the wheel.

      - Stand in front of the wheel when you turn on the grinder.

      - If the grinder begins to vibrate, make strange noises, or smoke, stop the machine and tell the instructor at once.

      - Always wear gloves when using the pedestal grinder but keep hands and fingers out of the way of the moving wheel.

DRILL PRESS SAFETY TEST

      - The drill should be sharp and ground at the proper angle.

      - As a general rule, the larger the bit sizes the slower the speed.

      - When drilling metal, use a center punch to mark the starting point of the drill.

      - When drilling metal, use a pilot hole for holes larger than 1/2 inch.

      - The use of cutting oil is not needed when drilling mild steel.

      - Loose clothing is a must when operating the drill press.

      - When drilling long stock, place the long end to the left so it will hit the column, not the operator, should it slip or rotate.

      - Be sure the chuck is tight on the drill and that the chuck wrench has been removed prior to drilling.

      - Chips should be removed from the table with your fingers.

      - Gloves should be worn when using the drill press.

      - Long hair should be tied back to prevent it from getting caught in the chuck.

      - The drill speed is the same for all types of work.

      - If the drill suddenly stops while you are drilling, and you did not stop the motor, the first thing you should do is shut the drill press off.

OXYACETYLENE SAFETY TEST

      - The cylinders should always be securely held in an upright position.

      - Oil or grease may be used to lubricate fittings around the regulator.

      - The do not stand in front of regulator gages while opening cylinder valve.

      - Store and use oxyacetylene rigs in well-ventilated areas.

      - Line pressure for acetylene should never exceed 15 pounds per square inch.

      - The acetylene cylinder valve should only be opened 1/4 to 1/2 turn.

      - A cigarette lighter is excellent for lighting the acetylene torch.

      - The torch may be used to dust off clothing or a workbench.

      - Acetylene and oxygen regulators may be switched.

      - The regulator adjusting screw should be opened slowly or loosened before opening the cylinder valve.

      - Test for leaks with soapy water, not matches.

      - Prevent heat and sparks from getting to hoses and cylinders.

      - Oxyacetylene goggles should be worn when cutting or welding.

      - A cylinder should never be used as a ground in an electrical circuit.

      - Empty cylinders should be marked and designated as such.

      - Always replace the cylinder cap when not in use.

PORTABLE GRINDER SAFETY TEST

      - The grinder should be held with both hands while in use.

      - A face shield, safety glasses and proper dress are necessary while operating or observing the grinder.

      - If sparks are discharged toward someone, small pieces small pieces of metal may become imbedded in the skin and could cause burns.

      - The grinder should be placed on its side so that nothing touches the abrasive disc while it is not in use.

      - It is permissible to leave the grinder on the ground while the disc is still turning.

      - The grinder speed should not exceed the speed printed on the abrasive disc.

      - The power should be disconnected before making adjustments or changing the disc.

      - Make sure all small stock is clamped securely before grinding.

      - Using the grinder near flammable materials should be avoided.

      - The power cord is insulated so it will not be damaged if it comes in contacted with the abrasive disc.

      - Discontinue use of the abrasive disc when it is cracked or becomes worn to less than 1/2 of its original diameter.

Check your answer key and make sure your last answer was #82

ARC/MIG/TIG WELDING SAFETY TEST

      - Give the word cover to all people standing before striking the arc.

      - The ground and electrode cables are constructed so that machines can run over them and objects will not penetrate the insulation.

      - Leather gloves and rubber soled boots should be worn in order to safely weld while standing in water or on wet surface.

      - Hot metal may be handled with gloves or hot metal tongs.

      - Welding should only be done in well-ventilated areas.

      - Welding should never be done in an area near or containing combustible materials.

      - When the electrode is burned close to the holder, it can be cooled with water.

      - The lens specification depends upon the amperage used and the type of welding being done, but a #10 lens is the best all-around lens for a HS shop facility.

      - Examine the helmet and lens before each use to check for cracks.

      - The electrode holder may be placed on the table, between the knees, or under the arm when not welding.

      - Proper dress for welding includes buttoned collars and cuff less pants.

      - Standing on ground metal when welding could be dangerous.

      - It is safe to observe welding from a distance with out eye protection.

BRAKE/SHEAR SAFETY TEST

      - You don't need permission to use the shear

      - Metal to be cut or punched should not exceed the limits of the machine.

      - It will not harm the blade to cut hardened metal.

      - All guards should be in place before cutting.

      - Safety glasses should be in place before cutting or punching metal.

      - Safety glasses and gloves should be worn when operating the shear and 			brake.

      - When using the punch, it should be checked first to make sure the punch 		and die do not hit.

      - Hands should be kept away from the machine while in use.

      - Metal should be clamped down tight before it is cut.

      - Small pieces of metal should be caught before they fall out of the machine.

Check your answer key and make sure your last answer was #105

PLASMA CUTTER SAFETY TEST

      - You must have the teacher’s permission before using the plasma cutter.

      - Touching the torch parts or the arc while the power is on will not hurt you.

      - Before using the plasma cutter set the air pressure at 100 psi.

      - Poor ventilation is not a problem when using the plasma cutter.

      - A number 5 lens or darker must be used when cutting.

      - The work piece should be properly grounded when working.

      - Do not touch the work piece when cutting.

      - Shut the power off and leave the air connected when finished cutting.

      - Use the plasma cutter on containers that have held combustible materials.

      - Hold the torch at an angle to pierce holes.

      - Do not use the plasma cutter if any parts are damaged or broken.

HAND AND POWER TOOL SAFETY

      - Sharp edged tools should be carried around in clothes pockets.

      - Using a wrench for a hammer is sometimes necessary.

      - When using a power tool be sure all safety guards are in place and 	functional.

      - Most hand tool injuries can be avoided just by choosing the right tool.

      - Be careful not to cut the power cord with a tool.

      - The power switch should be off and the tool should be stopped before 	laying it down.

      - All adjustments should be made with the tool turned on.

      - I realize that this test can not cover all safety rules/issues/or circumstances, 	but I will abide by all rules or instructions given during this course to 	insure my personal safety, fellow student’s safety, and the instructor’s 	safety at all times.  As well as make good judgment during the class and 	ask questions on things unknown or equipment I do not feel safe or 	comfortable operating.

      - I agree that I am a safe worker in the shop and will follow and observe the 	rules of this class and will use all safety rules in this test and other 	guidelines that may arise during the year.